1 η ΕΡΓΑΣΤΗΡΙΑΚΗ ΑΣΚΗΣΗ
ΓΙΑ ΤΟ ΜΑΘΗΜΑ "Εργαστήριο Μικροϋπολογιστών"

Κυριακόπουλος Γιάννης Α.Μ. :03117440
Παγώνης Γιώργος Α.Μ.: 03117030

1.LXI B,03E8H ;BC=1000 IN ORDER TO HAVE 1 SEC DELAY
MVI E,FFH ; TO START FORM 0 IN EVERY LOOP

START:
LDA 2000H ;A=(2000) TAKE THE INPUT
ANI 0FH ; ONLY USE 4 LSB
JZ START
MOV D,A ; D=4LSB

UP:
LDA 2000H ; STOP THE COUNTER IF THE MSB OFF
ANI 80H
JZ UP

INR E ; INR THE COUNTER
MOV A,E
CALL DELB ; DELAY 1 SEC
CMA
STA 3000H ; DISPLAY
CMA
CMP D ; IF YOU HAVE REACHED THE 4LSB START TO DECREASE
; THE COUNTER, ELSE INR THE COUNTER UNTIL YOU
;REACHED 4LSB
JNZ UP

DOWN:
LDA 2000H ; STOP THE COUNTER IF THE MSB OFF
ANI 80H
JZ DOWN

DCR E ; DCR THE COUNTER
MOV A,E
CALL DELB
CMA
STA 3000H ; DISPLAY THE COUNTER
CMA
CPI 00H ; UNTIL REACH ZERO
JNZ DOWN
JMP START
END

2.
IN 10H

START:
MVI A,00H ; INITIALISE THE POSITIONS ON THE DISPLAY
STA 0900H
STA 0901H
STA 0902H

READ_X:
CALL KIND
MOV B,A ; B=X

READ_Y:
CALL KIND
MOV C,A ;C=Y

MVI A,00H

MVI D,10H ; MUL THE X WITH 16 TO FORM THE NUMBER
LOOP16X:
ADD B
DCR D
JNZ LOOP16X
ADD C ; X*16+Y TO FORM THE NUMBER
; NOW WE HAVE TO SUN THE NUMBER TO HUD AND TENS
; AND THE SAVE THIW TO EACH POSITION IN THE DISPLAY
HUD: ; IF THE NUMBER IF GRATER THAN 100 ADD 1 TO HUD AND
;SUB 100 FROM THE NUMBER
CPI 64H
JNC ADD_HUD
TENS: ; SAME FOR THE TENS
CPI 0AH
JNC ADD_TENS ; THE REST NUMBER IS SMALLER THAN 10
;SO WE JUST SHOW THE REST
STA 0900H
JMP DISPLAY

ADD_HUD:
MOV B,A
LDA 0902H
INR A
STA 0902H
MOV A,B
MVI B,64H
SUB B
JMP HUD

ADD_TENS:
MOV B,A
LDA 0901H
INR A
STA 0901H
MOV A,B
MVI B,0AH
SUB B
JMP TENS

DISPLAY:
LXI D,0900H
CALL STDM
CALL DCD
JMP START
END

3.
LXI B,01F4H ; DELAY OF 0,5SEC B=500
MVI E,01H ; E IS THE POSITION OF THE TRAIN
MOV A,E
CALL DELB
CMA
STA 3000H ; SHOW THE FIRST POSITION

; START WITH THE LEFT ROTATION BECAUSE WE ARE ON THE 01 LSB OF THE
; BOARD
ROTATE_LEFT:
LDA 2000H ; CHECK IF THE MSB IS ON ,SO YOU STAY THERE ,
;ELSE MOVE ON
ANI 80H
CPI 80H
JNZ ROTATE_LEFT

LDA 2000H ; CHECK IF WE HAVE PRESS THE BUTTON ON NO
;WHEN WE ARE AT 1 LSB THEN YOU MOVE AT THE CORRECT DIRECTION
;ELSE WE MOVE IN THE INVERSE ONE
ANI 01H
JZ ROTATE_RIGHT_INVERSE

MOV A,E ; IF WE HAVE REACH THE END ON THE LEFT ONE WHEN WE HIT
;THE BUTTON TO CHANGE FROM THE INVERSE TO NORMAL WE GO
;TO THE ROTATE_RIGHT
CPI 80H
CALL DELB
JZ ROTATE_RIGHT

MOV A,E ;
RLC ; ROTATE LEFT THE TRAIN
MOV E,A
CMA
STA 3000H ; DISPLAY THE TRAIN
CMA
CALL DELB
CPI 80H ; WHILE WE DONT HAVE REACH THE END ON THE ROTATE_LEFT
;WE KEEP GOING ELSE WE MOVE TO ROTATE_RIGHT

JNZ ROTATE_LEFT
CALL DELB
JZ ROTATE_RIGHT

ROTATE_RIGHT:
LDA 2000H
ANI 80H
JZ ROTATE_RIGHT

LDA 2000H
ANI 01H
JZ ROTATE_LEFT_INVERSE

MOV A,E
CPI 01H ; CHECK IF WE HAVE PRESSED THE LSB ON THE 01H POSITION
; AND WE HAVE TO MOVE LEFT
CALL DELB
JZ ROTATE_LEFT

MOV A,E
RRC ; ROTARE RIGHT THE POSITION OF THE TRAIN
MOV E,A
CMA
STA 3000H ; DISPLAY IT
CMA
CALL DELB
CPI 01H
JNZ ROTATE_RIGHT ; WHILE THE HAVENT REACH THE LSB OF THE DISPLAY
; KEEP GOING , ELSE GO TO LEFT
CALL DELB
JZ ROTATE_LEFT

ROTATE_RIGHT_INVERSE:
LDA 2000H
ANI 80H
JZ ROTATE_RIGHT_INVERSE

LDA 2000H
ANI 01H ; CHECK IF THE LSB BUTTON IS UNPUSHED SO WE HAVE TO GO
; TO THE NORMAL ROTATION ONCE AGAIN
JNZ ROTATE_LEFT

MOV A,E
CPI 01H
CALL DELB
JZ ROTATE_LEFT_INVERSE

MOV A,E
RRC
MOV E,A
CMA
STA 3000H
CMA
CALL DELB
CPI 01H
JNZ ROTATE_RIGHT_INVERSE
CALL DELB
JZ ROTATE_LEFT_INVERSE

ROTATE_LEFT_INVERSE:
LDA 2000H
ANI 80H
JZ ROTATE_LEFT_INVERSE

LDA 2000H
ANI 01H
JNZ ROTATE_RIGHT

MOV A,E
CPI 80H
CALL DELB
JZ ROTATE_RIGHT_INVERSE

MOV A,E
RLC
MOV E,A
CMA
STA 3000H
CMA
CALL DELB
CPI 80H
JNZ ROTATE_LEFT_INVERSE
CALL DELB
JZ ROTATE_RIGHT_INVERSE
END